## Slide 1: Enabling Application-Based Fault Tolerance in Sparse Matrix Solvers
Simon McIntosh-Smith
James Price
HPC Research Group
simonm@cs.bris.ac.uk
j.price@bristol.ac.uk

## Slide 2: Sparse linear solvers
TODO: Introduce CG etc

## Slide 3: ABFT for sparse matrix computations
Most of the matrix elements are zero
Stored in a compressed format
Which elements are non-zero may change over time
Can't use the same approach as dense LA
So we need a different approach for sparse matrices to try and catch SDCs
This work has been undertaken as part of the FP7 Mont Blanc project

## Slide 4: Sparse matrix compressed formats
Sparse matrices are typically mostly 0
E.g. in the University of Florida sparse matrix collection (~2,600 real, floating point examples), the median fill of non-zeros is just ∼0.24%
Therefore stored in a compressed format, such as COOrdinate format (COO) and Compressed Sparse Row (CSR)
The University of Florida Sparse Matrix Collection, T. A. Davis and Y. Hu, ACM Transactions on Mathematical Software, Vol 38, Issue 1, 2011.

## Slide 5: COO sparse matrix format
Conceptually think of each sparse matrix element as a 128-bit structure:
  Two 32-bit unsigned coordinates (x,y)
  One 64-bit floating point data value
Observation 1: In a COO format sparse matrix, there is as much data in the indices as in the floating point values
x-coord
y-coord
64-bit value
0
31
32
63
64
127
Notes: Not usually stored this way, but makes it easier to explain.

## Slide 6: Protecting sparse matrix indices
It turns out almost all sparse matrices store their elements in index sorted order
Observation 2: We can exploit this ordering, along with the sparse matrix structure, to define a set of index relationships, or criteria, which can then be tested as elements are accessed

## Slide 7: Sparse matrix index criteria 1
For an m x n sparse matrix:
0 < xk ≤ m
0 < yk ≤ n
Does this help us?
Largest matrix in UoFlorida set: ~118Mx118M
Only uses bottom 27 bits of x and y indices
Top 5 bits (at least) must always be 0 (15%)
This has reduced the number of susceptible bits
Notes: Note that an error in the top bits might have caused erroneous pointer access, causing an application crash.
On average it's much better than this. Excluding the largest 13 matrices from the collection, the rest are only up to 16Mx16M, needing just 24 bits, so we've already protected the top 8 bits of each index, or 25% of the index data (12.5% of an entire sparse matrix element).
Moreover, these errors can be immediately corrected almost for free – just zero the top bits (could just always do this). Considerably cheaper than a checkpoint/restart.

## Slide 8: Sparse matrix index criteria 2
Exploit the ordering of sparse matrix elements:
xk-1 ≤ xk ≤ xk+1
yk-1 < yk when xk-1 = xk
where 1 < k < NNZ
Harder to evaluate how much these help us, as the answer depends on the distribution of the non-zeros in the matrix
Notes: If we have CSR format instead of COO then we actually have a couple of slightly different constraints we can use instead.
More constraints available when banded, symmetric etc.

## Slide 9: Distributions of non zeros
yk-1
yk
yk+1
When non zeros are very spread out, potentially many bits of yk could be flipped while still
satisfying the ordering constraint
yk-1
yk
yk+1
When non zeros are closer together, there are far fewer susceptible bits, i.e. bits of yk that can be flipped without the ordering constraint spotting the fault
Notes: In some cases when a bit has been flipped which violates the ordering constraint, there is only one possibility for which bit has been flipped. In these cases the error can be trivially and cheaply corrected just by re-flipping the bit.
For example, if non-zeros were on average about 512 elements apart, then there'd be about 10 bits that would be "susceptible" per index, as one or more of the bottom 10 bits could be flipped, and the index would still be within its original boundaries. The index could therefore be corrupted by [-512..+511] without changing the ordering of the indices.
However, when the indices are close, say around 16 apart on average, then only the bottom 5 bits of the index are susceptible, and if any other bits are flipped then the ordering constraint would catch the error.

## Slide 10: Non zero distributions
Most real-world sparse matrices contain a lot of "clumping" of the non-zeros
"nasasrb"
"circuit5M"

## Slide 11: Results from "nasasrb"
Nearly 70% of all indices fully protected
All indices have at least 17 of their 32 bits protected
~55Kx55K, 0.1% non-zero
Notes: nasarb is of average size in the collection –
---- 54,870 x 54,870 (~3,000,000,000 potential positions)
---- nnz = 2,677,324 (which is ~0.09% fill)
---- any other data you may want: https://www.cise.ufl.edu/research/sparse/matrices/Nasa/nasasrb.html

## Slide 12: Results from "circuit5M"
About 45% of all indices fully protected
All indices have at least 9 of their 32 bits protected
~5.5Mx5.5M, 0.0002% non-zero
Notes: circuit5M is one of the largest real matrices in the collection –
---- 5,558,326 x 5,558,326 (~30,000,000,000,000 potential positions)
---- nnz = 59,524,291 (which is ~0.0002% fill)
---- any other data you may want: https://www.cise.ufl.edu/research/sparse/matrices/Freescale/circuit5M.html

## Slide 13: Exploiting index constraints
Most constraints can be implemented with very simple integer operations
  Arithmetic, bit shifts, comparisons
These can be implemented in just a few instructions on most modern computer architectures
Sparse matrix element accesses tend to cause cache misses
  Opportunity to perform constraint checks in parallel with long latency DRAM accesses
A prototype implementation has the constraints checking overhead down to ~10%
Notes: Thus we believe we should be able to hide the cost of most of the constraint checking, making this a very low overhead approach
The overhead is all compute, there's no extra bandwidth required, and we think we can get this down lower.

## Slide 14: Going beyond index constraint checking
Advantages of approach:
Fast to test, enables some correction
Software implementation
Catches majority of SDCs in index bits in a fine-grained in time and space manner
Disadvantages:
Doesn't catch all index bit errors
Only protects the indices, not the data

## Slide 15: Software ECC protection for sparse matrix elements
Remember that most sparse matrices only use up to 27 bits of their 32-bit indices
  And most only use 24 bits
Observation 3: This leave 10-16 bits that could be "repurposed" for a software ECC scheme
A software ECC scheme could save considerable energy, performance and memory (all in the region of 10-20%)
Notes: At Exascale, 10-20% could represent a couple of MegaWatts and millions of dollars per year.
Architectures such as GPUs already have the ability to selectively turn off ECC on external memory to save energy and increase performance.

## Slide 16: COO sparse matrix format
Using 8 bits of the 128-bit compound element would allow a full single error correct, double error detect (SECDED) scheme in software
Use e.g. 4 unused bits from the top of each index
  Limits their size to "just" 0..227 (0..134M)
Requires no more bandwidth, just more compute
  Actually saves the 12.5% ECC bandwidth…
x-coord
y-coord
64-bit value
0
31
32
63
64
127
Notes: It's a bit more complicated than this:
The bits can't be grouped as shown for a parity scheme to work
Instead have to be distributed through the fields that need protecting
Would require some construction/deconstruction as elements are accessed, but again just rudimentary instructions such as bit ops, shifts etc

## Slide 17: Software ECC
TODO: Go into much more detail about all the different flavours of software ECC
TODO: Discuss implementation details, performance results etc

## Slide 18: Software ECC exercise
TODO: hands-on exercise – implement ECC in simple CG using some library routines

## Slide 19: Conclusions
TODO: Conclusions