## Slide 1: Enabling Application-Based Fault Tolerance in Sparse Matrix Solvers
James Price
Simon McIntosh-Smith
HPC Research Group
j.price@bristol.ac.uk
simonm@cs.bris.ac.uk

## Slide 2: Sparse linear solvers
Often need to solve large systems of linear equations
  Finite difference / finite element methods
  Structural analysis
  Circuit analysis
Typically solving systems of the form:
  Ax = b
    Where A is a known matrix, b is a known vector, and x is the unknown vector that we wish to compute

## Slide 3: Sparse linear solvers
These systems will often involve extremely large matrices, that contain mostly non-zero values
  Generally <1% of elements are non-zero
Iterative solvers such as Jacobi or Conjugate Gradient are suitable for solving these large, sparse systems
  Direct approaches are not feasible when the matrix dimensions are very large
Notes: We’ll use CG for the exercise

## Slide 4: Sparse linear solvers
Even for very sparse matrices, the majority of the application data will be in the matrix
  0.01% of a 10M x 10M matrix is three orders of magnitude larger than a 10M element vector
This means that:
  Sparse matrix-vector products (SpMV) will account for the majority of the runtime in these iterative solvers
  The sparse matrix data will be the most likely candidate for suffering a silent data corruption (SDC)
Notes: 10B non-zeros in 0.01% of 10Mx10M matrix

## Slide 5: ABFT for sparse matrix computations
Since most of the matrix elements are zero, sparse matrices are stored in a compressed format
Which elements are non-zero may change over time
Can't use the same approach as dense LA
So we need a different approach for sparse matrices to try and catch SDCs
This work has been undertaken as part of the FP7 Mont Blanc project

## Slide 6: Sparse matrix compressed formats
Sparse matrices are typically mostly 0
E.g. in the University of Florida sparse matrix collection (~2,600 real, floating point examples), the median fill of non-zeros is just ∼0.24%
Therefore stored in a compressed format, such as COOrdinate format (COO) and Compressed Sparse Row (CSR)
The University of Florida Sparse Matrix Collection, T. A. Davis and Y. Hu, ACM Transactions on Mathematical Software, Vol 38, Issue 1, 2011.

## Slide 7: COO sparse matrix format
Conceptually think of each sparse matrix element as a 128-bit structure:
  Two 32-bit unsigned coordinates (x,y)
  One 64-bit floating point data value
Observation 1: In a COO format sparse matrix, there is as much data in the indices as in the floating point values
x-coord
y-coord
64-bit value
0
31
32
63
64
127
Notes: Not usually stored this way, but makes it easier to explain.

## Slide 8: Protecting sparse matrix indices
It turns out almost all sparse matrices store their elements in index sorted order
Observation 2: We can exploit this ordering, along with the sparse matrix structure, to define a set of index relationships, or criteria, which can then be tested as elements are accessed

## Slide 9: Sparse matrix index criteria 1
For an m x n sparse matrix:
0 < xk ≤ m
0 < yk ≤ n
Does this help us?
Largest matrix in UoFlorida set: ~118Mx118M
Only uses bottom 27 bits of x and y indices
Top 5 bits (at least) must always be 0 (15%)
This has reduced the number of susceptible bits
Notes: Note that an error in the top bits might have caused erroneous pointer access, causing an application crash.
On average it's much better than this. Excluding the largest 13 matrices from the collection, the rest are only up to 16Mx16M, needing just 24 bits, so we've already protected the top 8 bits of each index, or 25% of the index data (12.5% of an entire sparse matrix element).
Moreover, these errors can be immediately corrected almost for free – just zero the top bits (could just always do this). Considerably cheaper than a checkpoint/restart.

## Slide 10: Sparse matrix index criteria 2
Exploit the ordering of sparse matrix elements:
xk-1 ≤ xk ≤ xk+1
yk-1 < yk when xk-1 = xk
where 1 < k < NNZ
Harder to evaluate how much these help us, as the answer depends on the distribution of the non-zeros in the matrix
Notes: If we have CSR format instead of COO then we actually have a couple of slightly different constraints we can use instead.
More constraints available when banded, symmetric etc.

## Slide 11: Distributions of non zeros
yk-1
yk
yk+1
When non zeros are very spread out, potentially many bits of yk could be flipped while still
satisfying the ordering constraint
yk-1
yk
yk+1
When non zeros are closer together, there are far fewer susceptible bits, i.e. bits of yk that can be flipped without the ordering constraint spotting the fault
Notes: In some cases when a bit has been flipped which violates the ordering constraint, there is only one possibility for which bit has been flipped. In these cases the error can be trivially and cheaply corrected just by re-flipping the bit.
For example, if non-zeros were on average about 512 elements apart, then there'd be about 10 bits that would be "susceptible" per index, as one or more of the bottom 10 bits could be flipped, and the index would still be within its original boundaries. The index could therefore be corrupted by [-512..+511] without changing the ordering of the indices.
However, when the indices are close, say around 16 apart on average, then only the bottom 5 bits of the index are susceptible, and if any other bits are flipped then the ordering constraint would catch the error.

## Slide 12: Non zero distributions
Most real-world sparse matrices contain a lot of "clumping" of the non-zeros
"nasasrb"
"circuit5M"
Notes: NSAS shuttle rocket booster
Freescale semiconductor circuit

## Slide 13: Results from "nasasrb"
Nearly 70% of all indices fully protected
All indices have at least 17 of their 32 bits protected
~55Kx55K, 0.1% non-zero
Notes: nasarb is of average size in the collection –
---- 54,870 x 54,870 (~3,000,000,000 potential positions)
---- nnz = 2,677,324 (which is ~0.09% fill)
---- any other data you may want: https://www.cise.ufl.edu/research/sparse/matrices/Nasa/nasasrb.html

## Slide 14: Results from "circuit5M"
About 45% of all indices fully protected
All indices have at least 9 of their 32 bits protected
~5.5Mx5.5M, 0.0002% non-zero
Notes: circuit5M is one of the largest real matrices in the collection –
---- 5,558,326 x 5,558,326 (~30,000,000,000,000 potential positions)
---- nnz = 59,524,291 (which is ~0.0002% fill)
---- any other data you may want: https://www.cise.ufl.edu/research/sparse/matrices/Freescale/circuit5M.html

## Slide 15: Exploiting index constraints
Most constraints can be implemented with very simple integer operations
  Arithmetic, bit shifts, comparisons
These can be implemented in just a few instructions on most modern computer architectures
Sparse matrix element accesses tend to cause cache misses
  Opportunity to perform constraint checks in parallel with long latency DRAM accesses
Notes: Thus we believe we should be able to hide the cost of most of the constraint checking, making this a very low overhead approach
The overhead is all compute, there's no extra bandwidth required, and we think we can get this down lower.

## Slide 16: Sparse matrix ABFT Results
Performance collected using a CG solver in TeaLeaf (hydrodynamics mini-app from Mantevo benchmark suite)
x86: Intel E5-2670, 16-cores @ 2.6GHz
ARM32: Samsung Exynos 5 dual Cortex-A15
Scheme | Bits needed | x86 overhead | ARM32 overhead
Constraints | 0 | 1.00x | 1.07x

## Slide 17: Going beyond index constraint checking
Advantages of approach:
Fast to test, enables some correction
Software implementation
Catches majority of SDCs in index bits in a fine-grained in time and space manner
Disadvantages:
Doesn't catch all index bit errors
Only protects the indices, not the data

## Slide 18: Software ECC protection for sparse matrix elements
Remember that most sparse matrices only use up to 27 bits of their 32-bit indices
  And most only use 24 bits
Observation 3: This leave 10-16 bits that could be "repurposed" for a software ECC scheme
A software ECC scheme could save considerable energy, performance and memory (all in the region of 10-20%)
Notes: At Exascale, 10-20% could represent a couple of MegaWatts and millions of dollars per year.
Architectures such as GPUs already have the ability to selectively turn off ECC on external memory to save energy and increase performance.

## Slide 19: COO sparse matrix format
Using 8 bits of the 128-bit compound element would allow a full single error correct, double error detect (SECDED) scheme in software
Use e.g. 4 unused bits from the top of each index
  Limits their size to "just" 0..227 (0..134M)
Requires no more bandwidth, just more compute
  Actually saves the 12.5% ECC bandwidth…
x-coord
y-coord
64-bit value
0
31
32
63
64
127
Notes: It's a bit more complicated than this:
The bits can't be grouped as shown for a parity scheme to work
Instead have to be distributed through the fields that need protecting
Would require some construction/deconstruction as elements are accessed, but again just rudimentary instructions such as bit ops, shifts etc

## Slide 20: Parity bits
Add an extra bit to data (or repurpose an unused bit)
Count number of ‘1’ bits in data
  If odd number, set parity bit to ‘1’
  If even number, set parity bit to ‘0’
  This is known as even parity
Can detect any odd number of bit flips
Can protect any number of data bits
Cannot correct corrupted data
This is a single-error-detect scheme (SED)
Notes: Correction could be done with checkpoint restart, or reload from second copy of matrix

## Slide 21: Parity bits - example
1
1
0
1
1
0
1
1
1
1
0
1
1
0
1
1
1
1
0
1
1
0
1
1
1
1
0
1
0
0
1
7 data bits
parity bit
five ‘1’ bits in data
odd number of ‘1’s: set parity bit to ‘1’
corrupted transmission (bit flip)
successful transmission
even number of ‘1’ bits (six) data is valid
odd number of ‘1’ bits (five) data is invalid

## Slide 22: Parity bits - implementation
Simple to implement with bitwise operations
  Mostly XOR (^ operator in C)
Some processors may have native hardware support for computing parity efficiently
Several compilers (gcc, clang, icc) support intrinsics to handle this

## Slide 23: Parity bits - implementation
uint32_t data[4]; // 128 bits of data
uint32_t p = data[0] ^ data[1] ^ data[2] ^ data[3]
p ^= p >> 16;
p ^= p >> 8;
p ^= p >> 4;
p ^= p >> 2;
p ^= p >> 1;
// p is now ‘1’ or ‘0’, corresponding to data having
// an odd or even number of ‘1’ bits

## Slide 24: Parity bits - implementation
uint32_t data[4]; // 128 bits of data
uint32_t p = data[0] ^ data[1] ^ data[2] ^ data[3]
// This intrinsic should map to native hardware
// implementation if available
p = __builtin_parity(p);
// p is now ‘1’ or ‘0’, corresponding to data having
// an odd or even number of ‘1’ bits

## Slide 25: Parity bits - implementation
uint64_t data[2]; // 128 bits of data
uint64_t p = data[0] ^ data[1];
// This intrinsic should map to native hardware
// implementation if available
p = __builtin_parityl(p);
// p is now ‘1’ or ‘0’, corresponding to data having
// an odd or even number of ‘1’ bits

## Slide 26: Sparse matrix ABFT Results
Performance collected using a CG solver in TeaLeaf (hydrodynamics mini-app from Mantevo benchmark suite)
x86: Intel E5-2670, 16-cores @ 2.6GHz
ARM32: Samsung Exynos 5 dual Cortex-A15
Scheme | Bits needed | x86 overhead | ARM32 overhead
Constraints | 0 | 1.00x | 1.07x
SED | 1 | 1.01x | 1.28x

## Slide 27: Hamming codes
A single parity bit can detect a single-bit flip, but gives us no ability to correct errors, or to detect multi-bit flips
Hamming codes extend the concept of parity bits to provide the ability to correct single-bit errors
They can be further extended with an additional parity bit in order to also detect (but not correct) double-bit errors
Notes: Invented by Richard Hamming (Bell labs) in 1950

## Slide 28: Hamming codes
Uses multiple parity bits
Each data bit is protected by a unique set of parity bits
The parity bits are also covered by this scheme
  This is achieved by placing the parity bits at ‘power-of-two’ positions in the data
k parity bits can protect a binary string of length 2k – 1 bits (or 2k – k – 1 data bits)

## Slide 29: Hamming codes
Parity bits are interleaved with data
Bit positions start from 1
Parity bit i protects bit positions with ith bit set
original data bits
bit positions
codeword
p1 protects
p2 protects
p3 protects
p4 protects
d7
d6
d5
d4
d3
d2
d1
d8
d9
p4
d4
d3
d2
p3
d1
p2
p1
d7
d6
d5
d8
d9
8
7
6
5
4
3
2
1
11
10
9
13
12
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
Notes: This illustrates the way that each bit is protected by a unique set of parity bits
e.g. if bit 9 flipped, will show up in parity bits 1 and 4

## Slide 30: Hamming codes
bit 1
bit 4
bit 2
bit 3
bit 5
bit 6
bit 7
bit 8
bit 9
bit 10
bit 11
parity bit 1
parity bit 3
parity bit 2
parity bit 4

## Slide 31: Hamming codes - example
1
1
0
1
1
0
1
7 data bits

## Slide 32: Hamming codes - example
1
1
0
1
1
0
1
1
1
0
1
7 data bits
1
1
0
8
7
6
5
4
3
2
1
11
10
9
Move data bits into their adjusted positions in codeword

## Slide 33: Hamming codes - example
1
1
0
1
1
0
1
1
1
0
1
1
7 data bits
1
1
0
8
7
6
5
4
3
2
1
11
10
9
Parity bit 1 protects bits 1,3,5,7,9,11…
three ‘1’ bits (odd), so make parity bit a ‘1’

## Slide 34: Hamming codes - example
1
1
0
1
1
0
1
1
1
0
1
1
7 data bits
1
1
0
8
7
6
5
4
3
2
1
11
10
9
Parity bit 2 protects bits 2,3,6,7,10,11…
five ‘1’ bits (odd), so make parity bit a ‘1’

## Slide 35: Hamming codes - example
1
1
0
1
1
0
1
1
1
0
0
1
7 data bits
1
1
0
8
7
6
5
4
3
2
1
11
10
9
Parity bit 3 protects bits 4,5,6,7…
two ‘1’ bits (even), so make parity bit a ‘0’

## Slide 36: Hamming codes - example
1
1
0
1
1
0
1
0
1
1
0
1
7 data bits
1
1
0
8
7
6
5
4
3
2
1
11
10
9
Parity bit 4 protects bits 8,9,10,11…
two ‘1’ bits (even), so make parity bit a ‘0’

## Slide 37: Hamming codes - example
1
1
0
1
1
0
1
0
1
1
0
0
1
1
1
7 data bits
1
1
0
8
7
6
5
4
3
2
1
11
10
9
This is our final codeword

## Slide 38: Hamming codes - example
1
1
0
1
1
0
1
0
1
1
0
0
1
1
1
7 data bits
1
1
0
8
7
6
5
4
3
2
1
11
10
9
0
1
0
0
0
1
1
1
1
1
0
1
0
1
1
1
0
1
0
1
1
1
1
1
0
0
0
0
1
1
0
four ‘1’s (even) - OK
five ‘1’s (odd) - ERROR
one ‘1’s (odd) - ERROR
two ‘1’s (even) - OK
single bit flip at position 6
p1
p3
p2
p4

## Slide 39: Hamming codes
bit 1
bit 4
bit 2
bit 3
bit 5
bit 6
bit 7
bit 8
bit 9
bit 10
bit 11
parity bit 1
parity bit 3
parity bit 2
parity bit 4

## Slide 40: Hamming codes - example
1
1
0
1
1
0
1
0
1
1
0
0
1
1
1
7 data bits
1
1
0
8
7
6
5
4
3
2
1
11
10
9
0
1
0
0
0
1
1
1
1
1
0
Parity bits 2 and 3 failed the check
The position of the flipped bit has these two bits set
0
1
1
0
4
3
2
1
= 6 (in decimal)
Since we know bit 6 has been flipped, we can correct it

## Slide 41: Hamming codes
This gives us a single-error correct scheme (SEC)
Seven parity bits will protect a 127-bit codeword
  This means we can steal eight bits from the indices of our sparse matrix elements to give us full protection against single-bit errors
Requires significantly more computation than the single parity bit SED scheme

## Slide 42: Hamming codes - implementation
Interleaving the parity bits with the data will be very expensive
Instead, we can store the parity bits somewhere else, and just perform the hamming code operations as if they were in the correct (power-of-two) positions
If we store the parity bits in the unused high-order bits of the matrix indices, masking them out becomes a simple bitwise AND operation
We can precompute some masks for efficient extraction of the correct bits

## Slide 43: Hamming codes - implementation
uint32_t data[4]; // 128 bits of data
// calculate first parity bit
x = (data[0] & ECC7_P1_0) ^ (data[1] & ECC7_P1_1) ^
(data[2] & ECC7_P1_2) ^ (data[3] & ECC7_P1_3);
p1 = __builtin_parity(x);
// calculate second parity bit
x = (data[0] & ECC7_P2_0) ^ (data[1] & ECC7_P2_1) ^
(data[2] & ECC7_P2_2) ^ (data[3] & ECC7_P2_3);
p2 = __builtin_parity(x);
// etc
Notes: Masks will change if you change where you store the parity bits

## Slide 44: Sparse matrix ABFT Results
Performance collected using a CG solver in TeaLeaf (hydrodynamics mini-app from Mantevo benchmark suite)
x86: Intel E5-2670, 16-cores @ 2.6GHz
ARM32: Samsung Exynos 5 dual Cortex-A15
Scheme | Bits needed | x86 overhead | ARM32 overhead
Constraints | 0 | 1.00x | 1.07x
SED | 1 | 1.01x | 1.28x
SEC 7-bit | 7 | 2.61x | 4.27x

## Slide 45: Hamming codes - optimisation
Even with this optimisation, we are still performing eight 32-bit integer operations for each parity bit
This is still too expensive
We can further reduce the overheads by adding one more parity bit which covers the whole codeword
We can use this extra bit to check whether or not an error has occurred
Only if this overall parity check fails will we check the other seven parity bits to work out which bit contains the error
Notes: Since data corruption should be very infrequent, we will very rarely pay the full cost of checking all 7 parity bits

## Slide 46: Hamming codes - optimisation
uint32_t data[4]; // 128 bits of data
overall_parity = compute_overall_parity(data);
if (overall_parity != 0)
{
syndrome = compute_hamming_bits(data);
if (syndrome != 0)
{
// correct flipped bit
}
else
{
// correct overall parity bit
}
}

## Slide 47: Sparse matrix ABFT Results
Performance collected using a CG solver in TeaLeaf (hydrodynamics mini-app from Mantevo benchmark suite)
x86: Intel E5-2670, 16-cores @ 2.6GHz
ARM32: Samsung Exynos 5 dual Cortex-A15
Scheme | Bits needed | x86 overhead | ARM32 overhead
Constraints | 0 | 1.00x | 1.07x
SED | 1 | 1.01x | 1.28x
SEC 7-bit | 7 | 2.61x | 4.27x
SEC 8-bit | 8 | 1.04x | 1.48x

## Slide 48: Hamming codes - SECDED
An alternative use of this overall parity bit would be to detect double-bit errors (SECDED)
If the overall parity passes, but one of the other parity checks fails, then we have suffered a double-bit error
  We cannot correct this error, but we can fail gracefully
This requires that we always check all eight parity bits, so this is an expensive scheme
If we can assume that double-bit errors will always be consecutive, then we can use two overall parity bits to make this more efficient
  One will cover odd numbered bits, the other even numbered bits
  This now requires nine bits in total

## Slide 49: Hamming codes - SECDED
uint32_t data[4]; // 128 bits of data
overall_parity = compute_overall_parity(data);
syndrome = compute_hamming_bits(data);
if (overall_parity != 0)
{
if (syndrome != 0)
// correct flipped bit with hamming codes else
// correct overall parity bit
}
else if (syndrome != 0)
{
// report double-bit error
}

## Slide 50: Sparse matrix ABFT Results
Performance collected using a CG solver in TeaLeaf (hydrodynamics mini-app from Mantevo benchmark suite)
x86: Intel E5-2670, 16-cores @ 2.6GHz
ARM32: Samsung Exynos 5 dual Cortex-A15
Scheme | Bits needed | x86 overhead | ARM32 overhead
Constraints | 0 | 1.00x | 1.07x
SED | 1 | 1.01x | 1.28x
SEC 7-bit | 7 | 2.61x | 4.27x
SEC 8-bit | 8 | 1.04x | 1.48x
SECDED | 8 | 2.49x | 4.79x
Notes: Could run expensive schemes only every X iterations to reduce overheads (need checkpoint to fallback on)

## Slide 51: Software ECC
We cannot correct a double-bit error with the parity bits, but we could restore the matrix element from the original source (e.g. a file on disk)
Alternatively, we could combine ECC with a checkpoint/restart scheme
  Iterative solvers provide natural points at which to checkpoint (e.g. every X iterations)
To further reduce the overheads of ECC, we could also perform the checks only every X iterations

## Slide 52: Software ECC exercise
Using the provided CG code as a starting point, add ECC to make the code more tolerant to silent data corruption
There are two changes to make:
  Generate parity bits for each matrix element and store them in the high order bits of the column index
  Modify the SpMV function to check the parity bits and then correct any errors that are found

## Slide 53: Software ECC exercise
Comments in the code will guide you
  You just need to modify spmv.c
Two routines are provided to do the heavy lifting (see comments in common.h for descriptions):
  ecc_compute_col8
  ecc_correct_col8
To test the code, pass the ‘-x’ parameter to the application to inject a random bit-flip
Example solutions are provided

## Slide 54: Software ECC exercise
Extras (if you finish early!):
  Add an additional overall parity bit to improve the performance of the error checking code
    Use the ecc_compute_overall_partity routine
  Or use the extra parity bit to implement a SECDED scheme (use ‘–xx’ flag to inject a double-bit flip)
  Try implementing the index constraints scheme discussed earlier instead of ECC